## Slide 1: Bar stimulus 2.0

## Slide 2: Stepper motor
Trinamic QSH2818-32-07-006
https://www.trinamic.com/products/drives/stepper-motors-details/qsh2818/
https://www.digikey.com/en/products/detail/trinamic-motion-control-gmbh/QSH2818-32-07-006/4843423

## Slide 3: Stepper motor
G k r b

## Slide 4: Driver
TMC2208 SilentStepStick
https://www.trinamic.com/support/eval-kits/details/silentstepstick/
https://www.digikey.com/en/products/detail/trinamic-motion-control-gmbh/TMC2208-SILENTSTEPSTICK/6873626

## Slide 5: Driver
Motor power supply: 5.5-36V

## Slide 6: Driver: setting the motor current
Check the motor current rating (0.68A phase current). The driver’s Irms output should not exceed this value.
The Irms output of the driver can be measured the Vref point. For this driver, the relationship is Vref = (Irms * 2.5V) / 1.77A. Vref should therefore not exceed 0.96V, but a safer value would be 90% of this value (0.86V)
3) With the motor disconnected from the driver, measure the Vref value on the driver and adjust the pot until it reads the desired value

## Slide 7: Step size
200 full steps 🡪 1.8 deg/step
3200 microsteps (@ 16 microsteps) 🡪 0.1125 deg/microstep
200 microsteps = 22.5 degrees

## Slide 8: Wiring
5.5-36V
>1.4A
(I use 9V, 2A supply)